## Slide 1
The Fermi Gamma-ray Space Telescope: Spacecraft, operations and mission
Julie McEnery
NASA/GSFC

## Slide 2
The Fermi Observatory
Large Area Telescope (LAT)
Observes 20% of the sky at any instant, views entire sky every 3 hrs
20 MeV - 300 GeV - includes unexplored region between 10 - 100 GeV
Gamma-ray Burst Monitor (GBM)
Observes entire unocculted sky
Detects transients from 8 keV - 40 MeV
Huge improvement over previous missions in this waveband
  Increased effective area
  Improved angular resolution
  Broader energy range
  Wide field of view

## Slide 3: Survey mode
Rock north for one orbit and south for the next
Cover entire sky and always keep LAT FoV away from the Earth limb
Rotate about Z-axis to keep sun off the LAT radiators (on +-Y faces

## Slide 4
All Sky Coverage
In survey mode, the LAT observes the entire sky every two orbits (~3 hours).
Multiwavelength observations in coordination with the LAT are limited only by the ability to coordinate to other observations in other wavebands.
Can also perform pointed observations of particularly interesting regions of the sky.
LAT exposure over two orbits

## Slide 5: The Variable Gamma-ray Sky

## Slide 6: Fermi Highlights and Discoveries
Terrestrial γ-ray Flashes
GRBs
Fermi Bubbles
Nova
SNRs & PWN
Blazars
Radio Galaxies
LMC & SMC
Starburst Galaxies
γ-ray Binaries
Globular Clusters
Sun: flares & CR interactions
Pulsars: isolated, binaries, & MSPs
Unidentified Sources (577/1873)
Galactic
Extragalactic
e+e- spectrum
Notes: Pulsars – more subclasses of a known class

## Slide 7: Gamma-ray Burst Monitor
Detecting MeV transients from Earth, Sun, Galaxy and distant Universe
GBM is the most prolific detector of Gamma-Ray Bursts and Terrestrial Gamma-ray Flashes (thunderstorms) currently in orbit
2008
2009
2010
2011

## Slide 8: Observation modes
Normal Survey mode (default)
  1 orbit rock north, 1 orbit rock south, repeat
  Covers entire sky every two orbits (~3 hours)
  Efficient observing, LAT boresight stays away from the Earth.
Modified survey (improve exposure up to 2x)
  N orbits rock north, M orbits rock south, repeat
  Covers entire sky every N+M orbits
  Efficient observing mode
Target of Opportunity (improve exposure up to 4x)
  Allows rapid initiation of pointed mode observations
  Boresight traces earth limb while target is occulted.
  Least efficient observing mode (Significant occultation of LAT FoV by Earth)
Pointed mode (improve exposure up to 4x)
  Planned pointed mode observation
  Perform small segment of sky survey while target is occulted.
  Inefficient observing mode (some occultation)

## Slide 9
Observations summary
Almost exclusively in nominal data taking in survey mode
  50 deg rocking angle from May 27 2009 onwards
ARRs (~2/month)
  2.5 hours 5 Target of Opportunity Observations
  3C 454.3
  Crab Nebula flare (Sept 2010 and April 2011)
  Cygnus X-3
  Galactic Center
  Sun
2 modified survey mode observation
  Two orbits south, 1 orbit north to enhance coverage during PSR B1259 periastron
  Stay rocked north for 3 days to enhance observations of sun during solar activity
LAT Calibrations
  ~<12 hours/year

## Slide 10: Some Geometry
Path a source takes within the LAT FoV depends on its angle to the orbit plane, for the sun, this is the solar beta angle
50°
50°

## Slide 11: Sept 7, 2011
LAT pointing
  Dark region = occulted by Earth (z>113°)‏
  Blue line = LAT FoV (±66°)‏, White points = LAT events

## Slide 12: March 2012

## Slide 13: July 2012

## Slide 14
GLAST MISSION ELEMENTS
GN
HEASARC
GSFC
-
-
DELTA
7920H
•
White Sands
TDRSS SN
S & Ku
LAT Instrument Science Operations Center (SLAC)
GBM Instrument
Operations Center (MSFC)
GRB
Coordinates Network (GSFC)
•
Telemetry 1 kbps
•
-
•
S
Alerts
Data, Command Loads
Schedules
Schedules
Mission Operations
Center (GSFC)
Fermi Science
Support Center (FSSC)
•
m
sec
•
•
•
Fermi Spacecraft
Large Area Telescope
& GBM
GPS
Fermi MISSION ELEMENTS

## Slide 15: Data Latency
Mission Operation Center
GSFC
LAT Instrument Science Operations Center
SLAC
Fermi
GBM Instrument Operations Center
MSFC/NSSTC
Fermi Science Support Center
GSFC
Mission Operation Center
GSFC
Fermi
Fermi Science Support Center
GSFC
T 0
T 1
T 2
T 3
T 4
T 5
T 8
T 9
T 12
T 0
T 1
T 2
T 3
T 4
T 7
T 10
T 11
T 14
GBM DATA PATH
LAT DATA PATH
180m
+ 12m
+ 70m
+ 120m
+ 4m
+ 20m
+ 8m
+ 60m
= 474m
= 7h54m
White Sands Complex
White Sands Complex
180m
+ 12m
+ 70m
+ 120m
+ 26m
+ 60m
+ 26m
+ 60m
= 554m
= 9h14m
4.3Mbps
Level 0 processing
sometimes achieve higher bandwidth.
Nominal case, assuming no manual intervention or new calibrations.
Data ingest, conservative estimate
Data sit on SSR

## Slide 16: Data Latency
LAT - level 2 requirement: <72 hours from detection of gamma-ray photon to availability in public archive
  Typical latency is ~8 hours
  Everyone gets access to the data at the same time.
GBM Data is delivered to FSSC within 24 hours for routine data taking.
  GRB, Solar flares, TGFs - times, fluxes, location delivered in near real time.

## Slide 17: Fermi Science Support Center
Public data and extensive support for science Analysis Tools
http://fermi.gsfc.nasa.gov/ssc/
FSSC Supports Guest Investigator Analysis

## Slide 18: Fermi Users Group

## Slide 19: Questions?

## Slide 20
GRB090902B - Autonomous repoint
LAT pointing in celestial coordinates from -120 s to 2000 s
  Dark region = occulted by Earth (z>113°)‏
  Blue line = LAT FoV (±66°)‏, White points = LAT events

## Slide 21
Fermi Observatory
Large Area Telescope (LAT):
20 MeV - >300 GeV
2.4 sr FoV (scans entire sky every ~3hrs)
Gamma-ray Burst Monitor (GBM)
8 keV - 40 MeV
views entire unocculted sky
Launched on June 11, 2008

## Slide 22
Launch!
Launch from Cape Canaveral Air Station 11 June 2008 at 12:05PM EDT
Circular orbit, 565 km altitude (96 min period), 25.6 deg inclination.
Communications:
  Science data link via TDRSS Ku-band (40 Mbps, 8-10, 10 min contacts per day)
  S-band via TDRSS (8kbps) or ground stations (1.26 Mbps)

## Slide 23: Raw Data
Data consists of
  1.2 Mbps LAT data
  26 kbps GBM data
  51 kbps housekeeping data (from SC, LAT and GBM)
The onboard solid state recorder (SSR) has two partitions, read out in parallel
  Science (LAT+GBM data)
  Housekeeping
    Often arrives before science data due to smaller volume

## Slide 24: Where are we pointing (1)
3 star trackers (2 active, 1 spare)
  Acquires, tracks and identifies up to 6 bright stars in its FoV
Also have set of 4 gyroscopes that measure angular rates of the spacecraft
  Used to propagate attitude solution during star tracker outages (and between updates)
Propagated solution from the gyros is corrected by attitude measurements from the star trackers (similar to orbit location)
  Solution is robust to outliers and outages in star tracker measurements
  Track the residuals between star tracker measurements and propagated solution (always tiny compared with LAT psf)
Attitude solution reported at 5 Hz

## Slide 25: How do we know where we are?
GPS
  Propagate orbit model, refine orbit solution using GPS location data, data lying close to predicted location given higher weight (Kalman filter)
    Filtered solution robust against outliers or GPS outages
    Filtered solution more accurate than any individual GPS meas.
  Orbit location (from filter) reported at 1 Hz

## Slide 26: Absolute timing and orbit location
GPS also provides an absolute timestamp
  Used to calibrate an onboard oscillator.
Absolute timestamps are accurate to <300 ns (verified in ground test, and on orbit).
Orbit position determination good to ~<20 m
Both of these are important when considering very short timescales
  Millisecond pulsars!