GLAST GRB Simulations and Tracker Trigger Algorithm

High-Fidelity GRB simulations include:

( BATSE duration and peak flux distributions

( Peak flux scaled from BATSE to GLAST energies

( Number of pulses from BATSE GRB analysis

( Pulse-width distribution scaled to GLAST energies

( BATSE distribution of spectral power-law indices

( GLAST PSFs, effective area from Glastsim reconstruction

( Variation of PSF within GLAST field of view

( Average diffuse gamma background (~ 1 Hz)

( Simple on-board cosmic-ray background rejection (Level-3:  ~ 3 Hz)

Strawman Real-time, Unbinned Trigger Algorithm:

( Search sliding 20-event window – forming their N((N-1)/2 distances.

( Choose cluster for event with smallest average distance within 35( circle.

( Form joint spatial and temporal Likelihood for events within circle,

L  =  - log{ (((() ( (((t) } .

( Set threshold such that GLAST sees < 1 false trigger per ~ week.

Summary:  GLAST GRB Tracker Trigger Algorithm

( Unbinned (in time and space) approach fully exploits available information.

( Triggers on ~ 85% of BATSE-like bursts, ~ 233 / 270 (number per year).

( Triggers on ~ 78% of these bursts visible to GLAST in less than one second,

With fewer than one false trigger per 3 days.

( Refinements will include:

–  Spatial dependence of diffuse gamma flux

(Galactic Plane emission could dominate residual CR flux after L3T.)

–  Temporal dependence of on-board residual cosmic-ray flux

–  Reconsideration of L3T background rejection

( If trigger provided by GRB context instrument, then

recast 	unbinned trigger algorithm to use positional information,

and calculate probability of photon being associated with GRB

Regardless of trigger mode:  Must provide algorithm to determine association probability