;

;  Documentation for the IDL GRB simulator, GRBfullsim.pro, extracted from its comment lines.

;

;  Author:	Jay Norris

;  Date:	September 15, 2000

;

;  Overview:

;  (1) The main routine calls GRBglobal; sets up arrays; loops through the number of bursts to be

;        generated, calling makeGRB for each burst; optionally records the photon list per burst in

;        an output file; optionally plots the burst time profile.

;  (2) Module GRBglobal computes the number of bursts/year (Nbsim) within GLAST FOV

;        and calls procedures { get_durs, get_fluxes, get_plaws } which return Nbsim samples from

;        each of the distributions { durations, peak fluxes, power-law indices }, respectively.

;  (3) Module makeGRB computes the number of photons for this burst, and calls maketimes.

;  (4) Module maketimes makes BATSE-like time profiles, but with pulse widths extrapolated to

;       GLAST energies, generated in a call to module pickwidth; photons are distributed within a

;       given pulse according to an energy-dependent formulation.

;

pro GRBglobal, iseed, Zen_Norm

;

;  The program computes the number of bursts per year expected in the GLAST

;  field of view.  It then calls procedures which return samples from global

;  distributions for GRBs:  durations, peak fluxes, and power-law indices.

;  INPUT:

;  none

;  OUTPUT:

;  durs, the duration array

;  dur_gt2s, flag indicating if duration is {<>} 2 seconds

;  Frats, the array of ratios of peak flux to maximum

;  Fp, the array of ratios of peak fluxes

;  betas, the array of power-law indices

;  Nbsim, the number of bursts to manufacture

;

;  Assume zenith acceptance angle = 75 degrees, 810 bursts/yr all-sky,

;  and scanning mode.  Then we simulate in this solid angle acceptance

;  Nbsim bursts per year.

pro makeGRB, isim, Ethres, iseed, madeburst

;

;  Computes number of photons for this burst, N_inc:

;      SpecNorm units, integrated Peak Flux:  photons cm^-2 s^-1 (> Ethres).  Researches on normalization:

;      (1) Bonnell's fits to bright BATSE bursts; (2) comparison with EGRET norms for bright bursts –

;     Catelli's, Dingus' and Schneid's works; and definitively (3) analysis of Preece et al. spectroscopy catalog

;     of bright BATSE bursts (see JPN routine Specanal.pro).

;

;      The cofactors for SpecNorm are:  (a) {average flux / peak flux} =~ 1/7;

;      (b) scaling by (peak_flux)^1.5, determined from inspection of Preece et al.;

;      (c) duration (seconds); (d) 282743 cm^2 (6-meter dia. illuminated disk);

;      (e) scaling to integral above Ethres (e.g., 0.03 GeV) for case beta = -2;

;      (f) dispersion (dynrange) to approximately replicate the scatter in peak flux

;          vs. normalization at 1 MeV as estimated from Preece et al. catalog; and

;      (g) a dependence on power-law index as estimated from Preece et al. catalog.

;

;  Thus, N_inc is number of photons normally incident on projected disk of GLAST illumination sphere,

;  integrated above Ethres, for chosen peak flux & duration.  Energies distributed as power-law, index beta.

;  INPUTS:  (1) Ethres, minimum energy photon for set of simulated bursts; (2) Frats(isim), ratio of this

;  burst's peak flux to the maximum; (3) duration, this burst's total duration, (4) beta, this burst's

;  power-law index; (5) Npuls, this burst's number of pulses.

;  OUTPUTS:

;  The program returns:

;  Specnorm, the spectral normalization described above

;  N_inc [Nphotons(isim)], the total number of photons for which times will be chosen

;  GRBenergies, the array of photon energies

;  madeburst, a flag {y,n} indicating whether or not a burst was made

pro get_durs, iseed

;

;  The program chooses durations from the BATSE bimodal duration distribution,

;  where the measurement process is described by Bonnell et al. (1997, ApJ, 490, 79).

;  The parent sample is same as for peak fluxes:  from GRB 910421 (trig# 105) to

;  GRB 990123 (trig# 7343).  This partial sample (1262) includes bursts where

;  backgrounds could be fitted, and peak fluxes subsequently measured.

;  The sample spans 7.75 years.

;  INPUTS:

;  none

;  OUTPUTS:

;  The program returns a float array of durations (durs), and an integer array

;  (dur_gt2s: 0 or 1) indicating whether the burst's duration is from the

;  long mode (1) or short mode (0); this array is used to determine which

;  peak-flux distribution to choose from.  Size of returned arrays = Nbsim.

pro get_fluxes, iseed

;

;  The program chooses peak fluxes from the BATSE log N - log P; see Bonnell

;  et al. 1997, ApJ, 490, 79, which duplicates the procedure specified by

;  Pendleton*.  The measurement procedure is applied uniformly for that part

;  of the BATSE sample from GRB 910421 (trig# 105) to GRB 990123 (trig# 7343).

;  (*Pendleton used a different PF estimation technique for the initial BATSE Catalog.)

;

;  This partial sample (1262) includes bursts where backgrounds could be fitted,

;  and peak fluxes subsequently measured.  It spans 7.75 years.  Therefore,

;  in order to draw from a PF distribution representing 1 year, we truncate

;  at the eighth brightest burst in 7.75 ~ 8 years.  The peak flux measure

;  in Bonnell et al. is for 256-ms accumulations.

;  INPUTS:

;  The integer array dur_gt2s (0 or 1) indicating whether the burst's duration

;  is from the short mode (0) or long mode (1).  This array is used to determine

;  which peak-flux distribution to choose from, {N,P} for longs, {M,Q} for shorts.

;  OUTPUTS:

;  The program returns an array of peak fluxes (Fp), and an array of peak flux

;  ratios (Frats), normalized to the brightest burst in one year.

;  Size of returned arrays = Nbsim.

pro get_plaws, iseed

;

;  The program chooses spectral power-law indices from the BATSE power-law

;  distribution, as measured by Preece et al. (1999)

;  INPUTS:

;  none

;  OUTPUTS:

;  The program returns an array of power-law indices.

;  Size of returned arrays = Nbsim.

=================================================================

pro pickwidth, UnivFWHM, duration, Ethres, iseed

;

;  The program chooses a universal width for the pulses within a given burst.

;  A given GRB tends to have pulses of comparable widths.  Therefore (see Fig 3a

;  of Norris et al. 1996 "attributes" paper), pick one pulse width from the

;  distribution of fitted widths of "All" pulses, 50-300 keV, in bright, long

;  BATSE GRBs.  Then, since (a) ~ 1/4 of GRBs are short, and (b) short GRBs have

;  pulse widths ~ 1/10-1/20 that of long GRBs -- multiply pulse widths for one

;  quarter of the GRBs by compression factor of 1/10.  Then using Width ~ E^(-0.333)

;  relationship, scale chosen width to Ethres, from 100 keV.

;  INPUTS:

;  Ethres, the minimum energy photon for this set of simulated bursts

;  duration, this burst's total duration

;  OUTPUTS:

;  The program returns a FWHM width to be using in making pulses for one burst.

pro maketimes, GRBtimes, GRBenergies, N_inc, Npuls, duration, Ethres, iseed

;

;  make BATSE-like GRB time profiles, placing GLAST photons a la

;  cumulative BATSE intensity, but in narrower pulses:

;    (1) Npuls = number of pulses, proportional to BATSE duration.

;    (2) pulse peak amplitude is random (0.0=>1.0); sort amps in descending amp order.

;    (3) scramble amps of {1st,2nd} halves of pulses, separately (leaves profile asymmetric)

;    (4) center of pulse time is random within duration.  sort the times, ascending order.

;    (5) pulse width is drawn from BATSE width distribution for bright bursts (attributes

;        paper), scaled to GLAST energies, using width ~ E^-0.333 .

;    (6) make Npuls pulses with "bisigma" shapes => sum to produce time profile

;    (7) form cumulative distribution of BATSE intensity

;    (8) distribute the N_inc photons according cumulative intensity => GRBtimes

;    (9) offset the photon times according to (a) energy dependence, width ~ E^-0.333

;        and (b) time of peak, also proportional to E^-0.333.

;  INPUTS:

;  Ethres, the minimum energy photon for this set of simulated bursts

;  duration, this burst's total duration

;  N_inc, the total number of photons for which times will be chosen

;  GRBenergies, the array of photon energies

;  OUTPUTS:

;  The program returns:

;  Npuls, the number of pulses in this burst

;  amplitudes, the pulse peak amplitudes

;  tmax, the times of peak amplitude

;  GRBtimes, the array of photon times